## Slide 1
Presentation for DSN Group Meeting
By: Reza Faridmoayer
Supervisor: Dr. Asadi
Sharif University of Technology, Department of Computer Engineering
April 12, 2011
Exploration FTL Functionalities Through SSDmodel Source Code
&
Investigating the Input and Output Parameters of DiskSim

## Slide 2: Outline
Flash Translation Layer
Exploration Available FTL Functionalities through SSDmodel Source Code
Investigating the Input file of DiskSim Simulator
Investigating the output file of DiskSim Simulator
    Demonstrating different functionalities of DiskSim FTL by running different available options in DiskSim (Next Presentation)

## Slide 3: Flash Translation Layer (FTL)
SSD controller for handling three basic operations:
Read, write , and erase
FTL functionalities:
Address Mapping
Wear Leveling
Interleaving
Bad block management
Power-off-recovery
Page-mapping scheme
Block-mapping scheme
Hybrid-mapping scheme

## Slide 4: Exploration FTL Functionalities Through SSDmodel Source Code
Available Functionalities:
Address Mapping Page-mapping scheme
Wear Leveling
Interleaving
Unavailable Functionalities:
Bad block management
Power-off-recovery

## Slide 5: Exploration FTL Functionalities Through SSDmodel Source Code (Cont.)
Address Mapping
Page-mapping scheme
Advantage
Writing data to any free pages in flash memory Shows better performance
Disadvantages
Occupying Very large amount of memory space (both in RAM and flash memory)
Utilization garbage collection:
Increasing the number of copy and erase operations
Performance degradation

## Slide 7: Exploration FTL Functionalities Through SSDmodel Source Code (Cont.)
Mapping function
// void _ssd_write_page_osr
Wear Leveling
Three wear leveling algorithm:
Greedy-wear-aware
Greedy-wear-agnostic
Random (Not supported)

## Slide 8: Exploration FTL Functionalities Through SSDmodel Source Code (Cont.)
Greedy-wear-aware
Selecting the block with the oldest erase time as a coldest block
Selecting the block with the remaining lifetime less than retirement threshold
Migrating the valid pages
Cleaning the coldest block
Allocating the coldest block
//int ssd_pick_wear_aware_with_migration

## Slide 9: Exploration FTL Functionalities Through SSDmodel Source Code (Cont.)
Greedy-wear-agnostic
Creating the list of blocks with the least number of valid pages.
Selecting the block at the head of the list
Cleaning the selected block
Selecting the block with oldest erase time as a coldest block.
Migrating the valid pages from coldest block
Cleaning & allocating the coldest block
//static int ssd_pick_block_to_clean2

## Slide 10: Investigating the Input file of DiskSim Simulator
IOzone.parv as an example
Options | Comments
# A simple read-modify-erase-write policy = 1 # osr write policy =2 Write policy=2 | Mapping schemes
# Random = 1 (not supp), greedy = 2, wear-aware = 3 Cleaning policy = 2 | Wear Leveling algorithms
# Number of planes in each flash package (element) Planes per package = 8 | 
# Number of flash blocks in each plane Blocks per plane = 2048 | 
Flash chip elements = 8 | 
Page size = 8 | 
Pages per block = 64 | 

## Slide 11: Investigating the Input file of DiskSim Simulator (Cont.)
Options | Comments
# Changing the no of blocks from 16184 to 16384 Blocks per element = 16384 (1*8*2048) | 
# Simple concatenation = 1, plane-pair stripping = 2 (not tested), full stripping = 3 Plane block mapping = 3 | The blocks mapping on planes of an element.
# Copy-back enabled (1) or not (0) Copy back = 1 | 
# entire elem = 1, two dies = 2, four plane-pairs = 4 Number of parallel units = 1 | 
# each gang = 0, each elem = 1, each plane = 2 Allocation pool logic = 1 | Allocation pool
# Elements are grouped into a gang Elements per gang = 1 | 

## Slide 13: Investigating the Output file of DiskSim Simulator
Iozone.outv as an example
ssd #0 elem #0
SSD cleaning statistics
Total reqs issued: 1125180
Total_reqs_issued=read_total+write_total
Total time taken: 347662.760004
IOPS
(Tot_reqs_issued*1000)/(tot_time_taken)

## Slide 14: Investigating the Ouput file of DiskSim Simulator (Cont.)
Total cleaning reqs issued: 16228
no of times cleaning on this element
Total cleaning time taken: 24342.000000
Sum of cleaning time
Total pages migrated: 0
no of pages migrated
Clean IOPS: 666.666667
(Total cleaning reqs issued*1000)/(total cleaning time taken)
Overall IOPS: 3068.261815

## Slide 15: Investigating the Ouput file of DiskSim Simulator (Cont.)
(Total reqs issued*1000)/(Total cleaning time taken+ Total time taken)
Number of free blocks: 824
Number of free blocks in this element
Average lifetime: 49.009521
Average remaining lifetime on all of the blocks in the element
Plane Level Statistics
0:(2089) 1:(2041) 2:(1954) 3:(1959) 4:(2058) 5:(1952) 6:(2107) 7:(2068)

## Slide 16: Investigating the Ouput file of DiskSim Simulator
Block Lifetime Distribution
< 20 < 40 < 60 < 80 < 100 >= 100
0 0 0 1049 627 14708
Bucket size=6
Calculates the for each block of element
If the no erase in block
Else increment the th element of the array
0
1
2
3
4
5

## Slide 17: proposed method
Previous page mapping scheme with a new garbage collection technique
New garbage collection technique
Selects a new block from a pool of free blocks
Selects the block with minimum number of valid pages as a victim block
Copies the valid pages from the victim block to a free block.
Erase the victim block
Update the mapping table to the new block.

## Slide 18
?
THANK YOU FOR YOUR ATTENTION