## Slide 1: Power Model
Kaveh Ramezani (kaveh.ramezani@gmail.com)
Dsn.ce.sharif.edu

## Slide 2: introduction
Needs for energy reduction schemes in storage systems:
  Power management strategies
    Switch to lower power modes in idle prides.
      Lower rotation speed (in multispeed disks)
      Head unload (some Toshiba disks)
      Standby
      Sleep

## Slide 3: introduction
Needs for energy reduction schemes in storage systems:
  Estimate Energy consumption
    Implementation on a real model
      Problems
        Cost (Accurate and high-speed power meters)
        Analyze problems
    Simulation
      Dempsey
      Adaptive power management
      Stamp
      State-based power model (DR. manzares)

## Slide 4: introduction
Adams power model:
  Implemented on disksim.
  Adds standby power management simulation to disksim
  Has some problems
    Inaccurate energy consumption
    Destroys access time

## Slide 5: Power management scheme
Disksim regular states:
  Idle phase:
    Platters rotate in max speed
  Active phase:
    Platters rotate in max speed
    Additional activities to serve IO requests
      Seek
      Latency
      xfer
Idle
Active
Start serving an I/O request
end serving an I/O request

## Slide 6: Power management scheme
Power management scheme:
  States:
    Idle phase
    Active phase
    Standby phase
      Spindle motor turns off
      Other parts are active
    If (idle-time > break event time)
      Go to standby state
Idle
Active
Start serving an I/O request
end serving an I/O request
Idle time>BET
Cache miss
Standby

## Slide 7: Power management scheme
Problems:
  Plotter rotation stop/start
    Time overhead.
    Energy consumption penalty
  Solution:
    middle states:
      Spin-up state
      Spin-down state
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up
Idle
Active
Start serving an I/O request
end serving an I/O request
Idle time>BET
Cache miss
Standby

## Slide 8: Power management scheme
Implementation details:
  Timer
  Spin-down
    Sleep
  Spin-up
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up

## Slide 9: Power management scheme
Implementation details:
  Timer
    Use IdleTimerExpired
    calculate idle interval time
    If (idle time> BreakEvenTime)
      Initiate Standby state
      (call spin-down function)
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up
timer

## Slide 10: Power management scheme
Implementation details:
  Spin-down
    disk status: DISK_SPIN_DOWN
    Add spin-down energy to TotalTransEnergy
    Make new event and add to queue
      Type: SPIN_DOWN_COMP
      Time: current time + spin-down time
    When this event arrives
      Disk status: DISK_STANDBY
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up
timer

## Slide 11: Power management scheme
Spin-up
  Wakeup-Disk-Sleep
  Wakeup_Disk_SpinDown
  Wakeup-SpinUp
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Spin-down
Spin-up

## Slide 12: Power management scheme
Spin-up
  Wakeup-Disk-Sleep
    Change disk state to DISK_SPIN_UP
    Add spin-up energy to TotalTransEnergy
    Add sleep time to TotalSleepTime
    Make new event
      Type: SPIN_UP_COMP
      Time: CurrTime+SU time
    Return delay time
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up

## Slide 13: Power management scheme
Spin-up
  Wakeup_Disk_SpinDown
    Change disk mode directly to DISK_SPINUP
    Add spin-up energy to TotalTransEnergy
    Make new event
      Type: SPIN_UP_COMP
      Time: S-D-Com + spin-up-time
    Return spin_up_time as delay
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up

## Slide 14: Power management scheme
Spin-up
  Wakeup-Disk-SpinUp
    Return delay
    Delay=SU_Com – currtime
Idle
Active
Start serving an I/O request
end serving an I/O request
Standby
Idle time>BET
Cache miss
Spin-down
Spin-up

## Slide 15: Power management scheme
Important challenge:
When to call spin-up functions?
  in bus delay calculation function(Add spin-up/down overhead time to bus delay)?
    Problems:
      Inaccurate rotational latency
      Neglect internal buffer hit
  When i/o request arrives?
    Discard current req
    Make a new i/o req-event
      time= previous req-event time + delay
    Problem: neglect internal buffer hit
  After buffer miss and Before access phase( before initiate seek function)

## Slide 16: Energy consumption Measurement
Energy calculation methodology
  Estimate time of each state
  Each state energy consumption= state total time * state power
  States:
    Sleep
    Spin down
    Spin up
    Active
    idle

## Slide 17: Energy consumption Measurement
Active state:
  Disksim active models.
    Constant mode
    Accurate mode
      contains three stages:
        Seek
        Rotational latency
        xfer

## Slide 18: Energy consumption Measurement
Active state:
  Seek
    Seek time =Max (HeadSwitchTime , SeekTime) + Write SettleTime

## Slide 19: Energy consumption Measurement
Active state:
    Rotational latency
0 sector
BPT
APT

## Slide 20: Energy consumption Measurement
Active state:
    Xfer
0 sector
sector 0

## Slide 21: Energy consumption Measurement
Idle state:
    Add distance between two requests to Total Idle Time variable
    Idle time = EndSimTime - (TotalActiveTime + TotalSleepTime + TransTime)

## Slide 22: Simple example:
R/W | Req_size | Bck_num | Dev_num | Time
1 | 20 | 70000 | 0 | 9000
Req_time
=9000
t=5500
Idle Time=5500
SD_TIme=1500
T=7000
Sleep:2000
SU_TIme=10900
Active
time
power | type
10.2w | Idle power
13.5w | Active Power
13j | SpinDown energy
135j | SpinUp energy
2.5w | Sleep power
1500ms | SpinDown time
10900ms | SpinUp time
T=19900

## Slide 23: Simple example:
Active time:
  Seek time:
    Distancet=34
    )
6 | Surfnum
extracted | Seek Type
0.487 | Settling delay
0.176 | headSwitchTime
334 | Sectors per track

## Slide 24: Simple example:
Active time:
  Rotate time
      4660
0 sector
BPT
APT
100025 RPM | Speed

## Slide 25: Simple example:
Active time:
  Xfer time:
    begin: 195
    End: 215
     requested sectores are in one sector
0
begin
End

## Slide 26: Simple example:
(disksim idle time=5502)